| The Office of the Main Board of the Polish Red Cross asks for a price offer for the supply of 1) electronic equipment 12 laptops and 12 monitors with a docking station not being a public procurement: Ordered object: 1.Laptop 12 pcs: |
| --- |
| Category | Description |
| Computing performance | The processor is to provide hardware support for virtualization. It should score 10,000 points on the cpubenchmark.net/cpu_list.php test. PassMark Test Source - CPU Benchmarks will be updated on the day of sending invitations to tender. Equipped with min. 6MB cache. |
| Working memory | 16GB RAM DDR4 |
| Graphics performance | Integrated, with the possibility of dynamic memory allocation within the operating memory |
| Display | Size 14 ”with a resolution of 1920x1080 matt with LED backlighting, with an anti-reflective coating |
| Hard drive | Min. 240GB SSD M.2 PCIe NVMe |
| Equipment | a) Sound card integrated with the motherboard b) Integrated in the housing WiFi IEEE 802.11 n / ac card with technology enabling wireless transmission of image and sound to the TV (e.g. WiFi Direct) c) Integrated in the Bluetooth housing d) Keyboard in Polish programmer's layout e) Touchpad f) Possibility to connect a computer-monitor or computer-multimedia system via a full-size HDMI connector g) 3 USB ports, including min. 1 x USB-C h) Stereo microphone and headphone combo in / out i) Built-in speakers, microphone j) Built-in 720p web camera |
| Power | Battery life 6 hours External power supply 230V 50Hz |
| laptop weight | Not more than 1.75 kg with battery |
| Software | License Microsoft Windows 10/11 Pro PL 64-bit or other equivalent 64-bit operating system with the following features: • enable the installation of software: Microsoft Office 365/2021/2019/2016, Microsoft Teams; • provide support for the Microsoft .NET Framework (including 4.8) and enable the launch of applications that require this environment; • have at least the following elements localized in Polish: menu, multimedia player, help, system messages; • have a built-in help system in Polish; • have a graphical installation and configuration environment; • make it possible to make free updates and corrections as part of the operating system version via the Internet, a mechanism provided by the manufacturer of the system with a choice of installed patches and a mechanism for checking which of the corrections are needed; • provide online updates in Polish; • have a built-in firewall to protect Internet connections; system-integrated console for managing firewall settings and IP v4 and v6 rules; have support for most commonly used peripherals (printers, network devices, USB standards, Plug & Play, WiFi); Full support of the computer manufacturer during the warranty period in the form of a complete set of drivers available on the website. The activation key should be permanently saved in the BIOS and allow the Windows installer to read and activate it automatically. |
| Laptop case | The housing must enable the use of a physical security in the form of a metal cable (Kensington, Noble lock connector) or a padlock (an eyelet in the housing for installing a padlock) |
| Additional requirements | ) FLASH EPROM BIOS with energy saving routines and a plug & play mechanism by the hardware manufacturer b) The BIOS must contain non-erase information about the manufacturer, model and serial number of the computer c) Laptop equipped with Trusted Platform Module (TPM v 2.0) |
| Manufacturer's warranty | Manufacturer's warranty not shorter than 36 months at the customer's premises |
| 2. Monitor with docking station 12 pcs: |
| Diagonal of the displayed image: | 684,7 mm (27”) |
| Maximum predefined resolution | 2560 x 1440 at 60 Hz |
| Response time | 8 ms (standard); 5 ms (fast) - (gray to gray) |
| Technical data | PbP / PiP / KVM PbP (no) PiP (no) KVM (yes), automatic KVM switch |
| Possibility of serial connection | Yes |
| Compatible with Dell Display Manager application | Yes |
| Communication | 1 DP 1.4 (HDCP 1.4) port 1 HDMI 1.4 (HDCP 1.4) 1 USB Type-B (USB 3.2 Gen 1 upstream) 1 USB Type-C (alternate mode: DisplayPort 1.4, USB 3.2 Gen 1 upstream, charging up to 90 W) 1 USB Type-C downstream (15W), USB 3.2 Gen 1 (5Gb / s) 1 DP (in) port with MST technology 2 super-fast 5Gb / s USB ports (USB 3.2 Gen 1) 1 super-fast 5Gbps USB port (USB 3.2 Gen 1) with BC 1.2 charging technology at 2A (max.) |
| 1 x 3.5mm headphone jack | 1 RJ45 port |
| Technical data of the webcam | 5 MP RGB + IR, Windows Hello compatible Frame rate - 1920 x 1080 (Full HD) - up to 30 frames per second |
| Built-in microphone | 2 digital microphones |
| Built-in speaker | 2 x 5 W |
| Security | Security lock slot (cable lock sold separately) |
| Power | Voltage required 100-240 VAC / 50 or 60 Hz ± 3 Hz / 2.5 A (maximum) Temperature range Operating: 0 ° C to 40 ° C (32 ° F to 104 ° F) Storage: -20 ° C to 60 ° C (-4 ° F to 140 ° F) |
| Humidity range | In operation: 10% to 80% (non-condensing) Storage: 5% to 90% (non-condensing) |
| Manufacturer's warranty | Manufacturer's warranty not shorter than 36 months at the customer's premises |

The expected date of order fulfillment and place of delivery: 14 days from the date of placing the order - the seat of the ZG PCK Office, Warsaw, ul. Mokotowska 14.

Please send price offers (gross) by November 25, 2022 in electronic form to the following address: it@pck.pl

Deadline for the settlement of submitted bids: November 28, 2022.

The criterion for selecting the offer is the lowest price and compliance with the contract specifications

Please attach the current CEDG entry to the order.

All information regarding the performance of the contract can be obtained by calling 607 895 005